## Slide 1: WP1 — Market: sizing what Verdal can address, and locating the €25bn Board figure
27 July 2026
Verdal Group · VG-STRAT-2026-07 · Version 2, built 27 July 2026 for the interim readout of 8 September · Confidential — Board review

## Slide 2: Three constructions of €25bn are live and we assert none — but all of them sit three perimeter levels above the €7.1m a year a site host keeps
WP1 — MARKET
1
The Board's figure is real, and we cannot yet say which of three things it measures
No source cleanly produces “European EV charging market, €25bn, 2030”. Three come close: a cumulative build-out capex near €30bn, paid forecasts spanning US$15-34bn across three horizon years, and a McKinsey report matching the figure exactly while measuring mobility finance.
2
Whichever it is, it sits three perimeter levels above what a landowner keeps
Our own funnel values all European public charging at €19.2bn a year in 2030 — the same order of magnitude, built independently. Verdal's level is the fourth of four: 1/2,680th of that continental flow, and 1/103rd of its own segment.
3
At the fee we had to assume the prize is €7.1m, and the increment is €0.5m
1,100 stores at four bays turn 84 GWh a year. An assumed lease earns €6.6m, a 15% revenue share €7.1m, self-operation loses €17.7m. What matters is the increment, not the pool — and at the published benchmark, €15 to 51m, it turns negative.
4
Self-operation turns on an equipment choice WP2 has not made, not on demand
Break-even needs 139 kWh a bay a day against the 80 we assume and cannot source. Demand can clear it, but only 74% above that. Either equipment choice does it at today's throughput, worth €21m and €19m. WP1 must not rule it in or out.
5
Three of the five decisive inputs are already in Verdal's hands
The store list, the two lease agreements and the energy contract are listed in the RfP as available. The two to be measured are kWh per bay a year, which both operators meter, and three grid quotes. Three requests close a €45m range.
→ Test the figure on perimeter, not on arithmetic — then settle the lease fee and the charger spec before anyone rules any structure in or out.
Source: WP1 market model v2, Assumptions tab; Verdal Board paper, June 2026; Savills UK, Autumn 2024.

## Slide 3: The figure under test
01
What a €25bn European charging figure could measure, and at which level of the chain

## Slide 4: Charging figures circulate at four levels and only the fourth is money Verdal banks — and self-operation would put it on the third as well
THE FIGURE UNDER TEST
Level
What it measures
Whose revenue it is
Europe, 2030
1. Infrastructure capex
Hardware, installation and grid connection across every site type, highway corridors and fleet depots included
Equipment makers and installers
A CUMULATIVE build-out magnitude, not an annual flow — one of three constructions consistent with €25bn
2. Energy at the plug
The full value of electricity delivered through every public charge point in Europe
Mostly the energy supplier, though the operator keeps the spread
€19.2bn a year
3. Operator revenue
What the charge-point operator bills, gross, in the segment Verdal sits in
The operator — and Verdal too, under self-operation
€733m a year, grocery destination, six countries
4. Site-host margin
What a landowner keeps: a lease fee, a revenue share, or the margin on operating
Verdal, today under lease
€7.1m a year — 1/2,680th of the plug flow, 1/103rd of its own segment
→ Establish which level a figure belongs to before doing anything with it — and show both ratios, because someone in the room will compute the second one.
Source: WP1 model v2, tabs 1 and 4. Level 1 is a cumulative magnitude and is nowhere divided into an annual margin.

## Slide 5: Three constructions land within a factor of two of €25bn on three different horizon years, and the exact match measures mobility finance, not charging
THE FIGURE UNDER TEST
Candidate
Published figure and horizon
Level
Why it is not a site host's margin
Charging build-out capex
€30bn cumulative to 2030 for public charging, of an €80bn total (Société Générale). ACEA/McKinsey put the same object at €8bn A YEAR
1
Capex, not revenue, and it includes highway corridors. Two published constructions of one object differ by over 2x
Paid market research
US$15.1bn (Grand View, 2030, no longer reproducible), US$25.35bn (Market Data Forecast, 2034), US$34bn (Meticulous, 2032)
1 to 3
Methodologies undisclosed, scopes include residential, three horizon years. One house publishes US$25bn and US$671bn for the same year
McKinsey mobility finance
€25bn of new annual revenue by 2030, 11 October 2023, five countries: France, Germany, Italy, Spain, UK
None
Matches figure, currency and year exactly and measures loans and leases. Charging is 'about 1 percent of total 2030 revenue'
Our own construction
€19.2bn a year paid at the plug across all European public charging, built from IEA and Ember data
2
Not a market anyone earns — most passes to the energy supplier. Shown because it lands in the same order from an independent route
→ We do not assert which the Board used. The Board paper's own citation settles it in one line, and it is data-room request no.1.
Sources: Société Générale; ACEA/McKinsey Masterplan; Grand View; Market Data Forecast; Meticulous; McKinsey, 11 Oct 2023. All read at source.

## Slide 6: Europe's €19.2bn of plug revenue narrows to €7.1m in three steps, and the step the Board paper skips is the operator's 85%, not a cost of delivery
THE FIGURE UNDER TEST
EUROS PAID AT THE PLUG, NARROWED, €M A YEAR (2030)
19,152
EU public charging
−18,419
Other segments
−685
Other grocers
−40.4
Operator's 85%
7.1
Verdal margin
→ The Board is not wrong to have quoted €25bn — it measures a different thing. Say so as a perimeter difference, never as an error.
WHAT EACH STEP REMOVES
• €19.2bn a year is a flow; the Board's €25bn is a cumulative build-out.
• Two steps narrow a continent to €733m, then to Verdal's own €47.6m.
• The third is the one the paper skips: €47.6m billed, €7.1m kept.
WHAT THAT THIRD STEP IS NOT
• Not a cost of delivery: under a revenue share Verdal spends nothing.
• €40.4m is the operator's margin and risk, not an expense of ours.
• Under self-operation the same energy costs €65.3m to deliver.
Sources: IEA Global EV Outlook 2025; Ember 2026; WP1 model v2, tabs 1, 3 and 4; Verdal Board paper, June 2026.

## Slide 7: What Verdal can address
02
The pool, top-down from European electricity; the volume, bottom-up from 1,100 car parks; and what neither has screened

## Slide 8: Four steps take Europe's EV electricity down to 1.3 TWh of grocery destination charging, and three of the four are our judgement, not a published split
WHAT VERDAL CAN ADDRESS
EUROPEAN EV ELECTRICITY TO GROCERY, TWH (2030)
European EV power
115.0 TWh
-70 %
Public charging
34.5 TWh
-78 %
Destination
7.6 TWh
-70 %
Grocery
2.3 TWh
-43 %
In scope
1.3 TWh
→ A bounding exercise, not a measurement — the bottom-up build on the next page is the primary estimate.
WHERE THE FUNNEL IS SOLID
• Only one step is sourced: the IEA's 4.3% EV share of consumption.
• The 22% destination share of kWh is ours — Europe publishes points.
• The 30% grocery share has no source at all. It is judgement.
HOW WE WOULD FIRM IT UP
• One IEA data download replaces the first steps with a published figure.
• Ask both operators for kWh per bay a year on Verdal's own sites.
• Treat the funnel as the bound, the bottom-up build as the figure.
Sources: IEA Global EV Outlook 2025 (Stated Policies); Ember 2026; Statzon from EAFO data, end-2023; WP1 model v2, tab 1.

## Slide 9: Bottom-up, 1,100 stores at four bays turn 84 GWh a year — 6% of the pool, and every euro of it rests on a bay count Verdal has not supplied
WHAT VERDAL CAN ADDRESS
VERDAL VOLUME FROM ITS OWN ESTATE, GWH A YEAR (2030)
Total 84.3 GWh
DC bays 64.2 GWh
Bays 2,200
kWh/bay/day 80
Days 365
AC bays 20.1 GWh
Bays 2,200
kWh/bay/day 25
Days 365
→ Two unsupplied numbers — bays a site, and how many sites qualify — multiply through everything above them.
WHAT IS VERDAL'S, AND WHAT IS OURS
• 1,100 stores is the only figure in this deck that Verdal supplied.
• 4 convertible bays a site is ours. It is data-room request no.1.
• 80 and 25 kWh a bay a day are modelled; destination rates are unpublished.
WHAT THE CHECK CAN AND CANNOT PROVE
• 84 GWh is 6.5% of the six-country pool on our own funnel.
• Both routes share the same bay count, so their agreement is circular.
• Every euro on the following pages is earned on this volume and no other.
Sources: Verdal RfP, 15 July 2026 (site count); WP1 model v2, tab 2. Bays, eligibility, mix and throughput are explicit assumptions.

## Slide 10: No screen has been run on which car parks can take a charger, so 'addressable' still means the whole estate
WHAT VERDAL CAN ADDRESS
FOUR SCREENS NOT YET RUN ON THE 1,100-STORE ESTATE
1,100 stores — how many qualify?
None yet run
1
Car-park
Bays convertible
Capacity per site
→ How many bays?
2
Grid
Site capacity
Reinforcement cost
→ Which take 500 kW?
3
Title
Freehold or pitch
Landlord consent
→ Free to contract?
4
Exclusivity
Two agreements live
Terms unknown to us
→ Already committed?
→ WP3 owns this screen. Until it runs, every figure in this analysis is an upper bound on the estate as well as on the economics.
WHY THIS PAGE EXISTS
• The mandate asks what is GENUINELY addressable. A store count is not that.
• Site eligibility sits at 100% in the model — deliberately, so the gap shows.
• Savills prices its rents only for sites with 15,000+ vehicles a day.
WHAT IT WOULD TAKE TO CLOSE IT
• Halve the eligible estate and the operate loss halves too, to €8.9m.
• Grid connection for an 8-24 bay hub: £250,000-1,000,000 (Savills).
• The screen is a WP3 deliverable. WP1 owes the Board only the honesty.
Sources: WP1 model v2, Assumptions C17 and tab 5, driver 3; Savills Research, UK Commercial, Autumn 2024, read at primary 27 July 2026.

## Slide 11: What a site host actually earns
03
Three commercial structures on the same energy, the published benchmark that reverses the ranking, and what decides the operate case

## Slide 12: At the lease fee we had to assume, a revenue share beats today's structure by €0.5m a year, while operating the chargers loses €17.7m on the same energy
WHAT A SITE HOST ACTUALLY EARNS
VERDAL'S RESULT BY STRUCTURE, €M A YEAR (2030)
+7.1
Revenue share at 15%
+6.6
Lease the bays, as today
−17.7
Operate the chargers
→ Same energy, same prices — and the whole ranking depends on a lease fee we invented, which the next page tests.
WHAT THE THREE STRUCTURES ARE
• Leasing pays a fixed fee per bay and carries nothing. It is today.
• A revenue share earns about €0.5m more, same bays, same risk.
• Operating buys power, chargers and grid, and keeps what is left.
WHAT THIS PAGE DOES NOT SETTLE
• The lease bar is our placeholder. The two agreements decide the ranking.
• The operate bar assumes a spec WP2 has not chosen — see slide 15.
• None of the three prices footfall: Lidl charges €0.39 against €0.60.
Sources: WP1 model v2, tab 3; Eleport, Feb-2026; Eurostat nrg_pc_205 band IC series X_VAT, H2-2025; Interpath, May 2026.

## Slide 13: At the only published benchmark, read at source, today's lease earns €15m to €51m a year — so the answer to the Board's question may well be no
WHAT A SITE HOST ACTUALLY EARNS
WHAT 4,400 BAYS EARN UNDER EACH BENCHMARK, €M/YR (2030)
#
Name
€m a year
1
Savills landlord-funded, £10,000 a bay
51.4
2
Savills CPO-funded high, £5,000 a bay
25.7
3
Savills CPO-funded low, £3,000 a bay
15.4
4
Revenue share at 15% of gross
7.1
5
Our assumed lease, €1,500 a bay
6.6
→ Do not present an uplift without the two actual agreements — this is what the recommendation turns on, and it is one document away.
WHAT CHANGED SINCE OUR FIRST PASS
• The benchmark was contested and carried as Probable. It is now Verified.
• We had converted £13-22m into '€13-22m'. At £1 = €1.1693 it is €15-26m.
• And the same document carries a second structure we did not have at all.
WHY THIS IS NOT YET AN ANSWER
• UK-only, sterling, per bay, Autumn 2024 — the only one found in Europe.
• Priced for sites with 15,000+ vehicles a day. We have not screened ours.
• Against the benchmark low, the best alternative is €8.3m behind.
Sources: Savills Research, UK Commercial, Autumn 2024, read at primary 27 July 2026; ECB euro reference rate, same date; WP1 model v2, tab 3.

## Slide 14: Self-operation loses €17.7m on a high-power spec, and fixed cost per charger and per point does €42m of the €65m of damage
WHAT A SITE HOST ACTUALLY EARNS
Line
€m a year
What the line rests on
Gross charging revenue
47.6
PROBABLE — 84.3 GWh at €0.60/kWh DC and €0.45 AC (Eleport country medians, Feb-2026)
Delivered electricity
(15.7)
VERIFIED — Eurostat band IC, series X_VAT, H2-2025, six-country mean €0.186/kWh — network charges already inside it
Grid capacity increment
(0.8)
HYPOTHESIS — €0.01/kWh ABOVE the band average, not a second full charge. Not evidenced; three quotes would settle it
Payment, software, roaming
(2.4)
HYPOTHESIS — 5% of gross — no charging-specific disclosure found anywhere
Charger operations
(24.2)
PROBABLE — €19,000 per DC charger a year — Interpath's own modelling assumption, May 2026
Charger capital, amortised
(17.8)
PROBABLE — €180,000 per charger over 12 years — Interpath's central case, not the top of its range
Grid connection, amortised
(4.4)
HYPOTHESIS — €60,000 a site over 15 years. Savills gives £250k-1m for an 8-24 bay hub — the error runs against us
Self-operation result
(17.7)
Fixed cost per charger and per point, not the energy margin, decides it
→ Fixed cost per charger decides this — so the charger spec, which WP2 has not chosen, decides it too.
Sources: WP1 model v2, tab 3; Interpath, May 2026; Eurostat nrg_pc_205 band IC series X_VAT, H2-2025; Eleport, Feb-2026.

## Slide 15: Demand turns self-operation positive only above 139 kWh a bay a day — either equipment choice WP2 has not made does it at today's throughput
WHAT A SITE HOST ACTUALLY EARNS
SELF-OPERATION AGAINST EACH DRIVER ALONE, €M/YR (2030)
DC throughput
-29.8
6.3
40-160 kWh/day
Charger spec
-17.7
3.5
200 to 75 kW
Bays per site
-31.1
-11.1
8 to 2 bays
Bays per charger
-17.7
1
2 to 4 outlets
Base case -17.7
Range tested
-30
-20
-10
0
€m a year
Downside
Upside
→ The equipment decision, not the demand, decides this — and WP2 has not made it yet, so WP1 must not rule self-operation in or out.
WHAT ACTUALLY DECIDES THE OPERATE CASE
• Every fixed cost is per charger a year, so count and spec decide it.
• A destination-grade unit rather than a highway one is worth €21m.
• Four outlets a unit rather than two is worth €19m on its own.
WHAT SITS OUTSIDE THIS CHART
• Throughput does clear zero — but only 74% above what we can defend.
• Site eligibility: at 50% of the estate the loss halves, to €8.9m.
• All four bars are live formulas; in our first pass three were prose.
Sources: WP1 model v2, tab 5 section C; Interpath, May 2026; Fastned Annual Report 2025. Destination throughput is unpublished.

## Slide 16: Self-operation clears break-even in ten of forty-two combinations of bays and throughput, and every one of them needs a bay to turn at least 140 kWh a day
WHAT A SITE HOST ACTUALLY EARNS
OPERATE RESULT, €M/YR, BY BAYS X DC KWH/BAY/DAY
40
60
80
100
120
140
160
2 bays
3 bays
4 — base
5 bays
6 bays
8 bays
-17.1
-14.1
-11.1
-8.1
-5.1
-2.1
0.9
-23.4
-18.9
-14.4
-9.9
-5.4
-0.9
3.6
-29.8
-23.8
-17.7
-11.7
-5.7
0.3
6.3
-36.1
-28.6
-21.1
-13.6
-6.1
1.4
9.0
-42.4
-33.4
-24.4
-15.4
-6.4
2.6
11.6
-55.1
-43.1
-31.1
-19.1
-7.1
4.9
17.0
→ Below break-even more bays deepen the loss; only above about 140 kWh a bay a day does scale start to help.
HOW TO READ THE GRID
• Each cell is the annual result at that combination, high-power spec.
• Whole-estate break-even is 139 kWh a bay a day — 74% above our base case.
• 10 of 42 clear it, and every one needs 140 kWh a bay a day or more.
WHAT THE GRID DOES NOT SAY
• It is a threshold map, not a demand forecast. That is the honest output.
• On a destination-grade unit the whole surface lifts by about €21m.
• Fastned turns 150-200 kWh a bay a day — on motorway sites, not ours.
Source: WP1 model v2, tab 5 section B. Every cell recalculates from the Assumptions tab, and all 42 assume the high-power spec.

## Slide 17: Read as ranges, the three structures barely overlap — and the lease spans €6.6m to €51.4m on a benchmark question, not on an economic one
WHAT A SITE HOST ACTUALLY EARNS
RESULT BY STRUCTURE, RANGE AND DRIVERS, €M/YR (2030)
Range: low bound – midpoint – high bound
Lease the bays
assumed to Savills
Revenue share
10% to 25% gross
Operate
40 kWh to dest. spec
Overlap 6.6–11.6
Today, assumed fee 6.6
6.6
51.4
4.8
11.9
-29.8
11.6
-20
0
20
40
€m a year
→ The mandate asked for a range with its drivers, not a point estimate. This is it — and the widest range is the one evidence closes, not analysis.
HOW TO READ THE THREE RANGES
• The lease range is not economic. It is an evidence range on one fee.
• The revenue-share range is a negotiation range: no operator discloses one.
• Only the operate range is economic, and its spread is an equipment choice.
WHICH RANGE CLOSES FIRST
• Two lease agreements close most of a €45m range in one document.
• Operator throughput data closes the demand half of the operate range.
• The charger spec closes the rest, and WP2 owns that decision.
Sources: WP1 model v2, tab 5 section D; Savills UK Commercial, Autumn 2024; Interpath, May 2026. Every bound recalculates.

## Slide 18: What we do before 8 September
04
What the public record already tells us, the five inputs that decide the answer, and the one decision we would ask the Board to take

## Slide 19: The two charging estates with published economics agree — a supermarket site is worth a fifth of a motorway one, and the landlord out-earned the operator
WHAT WE DO BEFORE 8 SEPTEMBER
Fastned, Annual Report 2025
183.0 GWh across 406 stations — about 1,235 kWh a station a day, or 150-200 kWh a bay. Gross profit €0.53/kWh, network utilisation 13.2%. TESTS our 80 kWh a bay a day: Europe's hardest-working operator turns about twice it, on motorway sites that are the wrong archetype for a supermarket.
Fastned's own supermarket case
Its April 2026 investor presentation publishes a 2030 case for a SUPERMARKET site: 40 sessions a station a day, 30-minute dwell, and maximum revenue per station of €252k against €1,417k for a motorway site. TESTS the operate case: a competitor's sourced view that a grocery car park is worth a fifth of a motorway one.
Pod Point's Tesco estate, FY2024
The only supermarket charging P&L in the public domain. £7.672m of revenue and £1.784m of operating profit across 598 sites — £2,983 a site a year, £1,334 a chargepoint, and part of it is advertising. TESTS the Board's premise: profit per chargepoint sits BELOW the bottom of the Savills per-bay rent.
IEA, Global EV Outlook 2026
European public-network time-based utilisation of 10% in 2025 rising to 15% by 2035. The IEA publishes the charging split in charger UNITS, never in kWh. TESTS two things: no European kWh split by location exists, so three funnel steps stay judgement; and 10-15% utilisation is a ceiling on any destination site.
→ None of these is ours and none of them flatters our assumptions — which is why they belong in front of the Board rather than in an appendix.
Sources: Fastned Annual Report 2025 and investor presentation Apr-2026; Pod Point plc FY2024 RNS; IEA Global EV Outlook 2026.

## Slide 20: Five inputs decide this answer and Verdal holds three of them — the two to be measured are destination throughput and a real grid-connection quote
WHAT WE DO BEFORE 8 SEPTEMBER
1
1 — Convertible bays per site, and car-park capacity
Held by Verdal today; the RfP lists it as available. Every euro in the model scales off this one number, and it is currently an assumption of four. It is also what the site-eligibility screen needs first.
2
2 — The two current lease agreements
Held by Verdal today, and the highest-value document on this list: it moves the lease result across a €45m range. At the published benchmark today's structure already beats every alternative we model.
3
3 — Energy contract and site grid capacity
Held by Verdal today. It sets the delivered cost per kWh, where a six-country Eurostat mean stands in for a real contract, and whether a site can take a high-power connection without reinforcement.
4
4 — kWh per bay per year on Verdal's own sites
Held by the two incumbent operators, who meter every session. The largest hole in the analysis, and one request rather than a research programme. Our 80 kWh a bay a day is modelled, not measured.
5
5 — Three real grid-connection quotes, in three countries
Does not exist yet. We model €60,000 a site; the only citable published figure is Savills at £250,000-1,000,000 for an 8-24 bay hub. Three quotes bound it well enough to decide.
→ Three of the five cost nothing but a data-room request — send them this week, not after the interim.
Source: WP1 model v2, Assumptions tab. Items 1-3 are held by Verdal today; 4 and 5 must be measured. Benchmark: Savills, Autumn 2024.

## Slide 21: Three actions before 8 September decide whether the interim reports a threshold or a forecast, and we would ask the Board for a capped pilot, not capital
WHAT WE DO BEFORE 8 SEPTEMBER
Week 1 — send three requests
The store list with car-park capacity and convertible bay counts; both current lease agreements; the energy procurement contract and site grid capacity. The RfP lists all three as available today. Together they replace the largest assumptions in the model and the only Verdal figures we had to invent — the bay count, the lease fee and the delivered cost of energy.
Weeks 2-5 — collect what is missing
Ask both incumbent operators, through Verdal, for kWh delivered per bay per year on Verdal's own car parks — they meter every session, so the figure already exists. In parallel obtain three grid-connection quotes across three countries — the published range spans a factor of four — and design and cost a 10-store metered pilot to measure throughput and dwell rather than to earn a return.
Before 8 September — re-run
Re-run the model on the supplied bay counts and the actual lease terms, and hand WP3 the site-eligibility screen. Both change the size of the answer; only the lease terms change its direction. Refresh the IEA basis against Global EV Outlook 2026 while the model is open, and reconcile the six national EV parc series onto a single EAFO basis before WP3 scores countries.
8 September — one decision
Present the perimeter finding on evidence and on scope: the Board is not wrong to have quoted €25bn. Then take one decision only — authorise a capped 10-store pilot and open the lease renegotiation, rather than allocate rollout capital — before WP5 scores build, buy, partner and the operator-managed fourth option Aldi UK moved to in June 2026.
→ Our recommendation at the interim: do not allocate rollout capital — authorise a capped pilot and open the lease renegotiation once the two agreements are read.
Sources: Verdal RfP, 15 July 2026, sections 5 and 7; WP1 model v2; Aldi UK-Drax transition, June 2026, trade press.

## Slide 22: WP1 — Market